## Slide 1
Controller v2
Improved robustness for spiral trajectory tracking
New tuned gains + saturation limits | compared with Controller v1
PFE - Laboratoire DRIVE - Competence SIC

## Slide 2
New Parameters for Robustness (v1 → v2)
Gain | v1 | v2
KP_XY | 0.6 | 4.5
KD_XY | 1.0 | 5.0
KP_Z | 4.0 | 6.0
KD_Z | 3.0 | 5.0
KP_ATT | 8.0 | 25
KD_ATT | 4.0 | 8
KP_yaw | 2.0 | 2.0
KD_yaw | 2.0 | 2.0
Safety limits (saturation) — new in v2
Thrust U1 ∈ [1, 35] N (≤ 2× weight; no downward pull)
Tilt |φ_d|, |θ_d| ≤ 30°
Torques U2, U3, U4 ∈ [-5, +5]
Also new (method upgrades):
• acceleration feedforward • thrust tilt-compensation • exact tilt inversion
Result: steady-state tracking ~5 m (v1) → ~0.18 m (v2), within limits.

## Slide 3
Where the Constants Are Used — Formulas
1 · Horizontal loop (feedforward + PD)
a_x = a_d,x + KP_XY·(x_d - x) + KD_XY·(v_d,x - v_x) (a_y analogous)
uses KP_XY = 4.5, KD_XY = 5.0
2 · Thrust with tilt-compensation (saturated to [1, 35] N)
U1 = m·( g + a_d,z + KP_Z·(z_d - z) + KD_Z·(v_d,z - v_z) ) / (cosφ · cosθ)
uses KP_Z = 6.0, KD_Z = 5.0
3 · Desired tilt (exact inversion, saturated to ≤ 30°)
φ_d = arcsin( U_ex·sinψ - U_ey·cosψ ), θ_d = arcsin( ... / cosφ_d )
uses tilt limit 30°
4 · Attitude torques (saturated to [-5, +5])
U2 = (I_x / l)·( KP_ATT·(φ_d - φ) - KD_ATT·p - coupling ) (U3, U4 analogous)
uses KP_ATT = 25, KD_ATT = 8, KP_yaw = 2, KD_yaw = 2